SECTION 133423

# PART 1 – GENERAL

1.01	SUMMARY

Provide all labor, equipment and materials to furnish one prefabricated Security Guard Booth.

1.02 	Related work specified elsewhere

A.	Electrical service supply and connection.

B.	Site/foundation work.

C.	Unloading, placement, installation and anchoring.

D.	Plumbing & piping (if required).

1.3  	Submittals

- Upon award of order, manufacturer shall prepare and submit shop drawings for each different building required for this project. Drawings shall include elevations, section, floor plan, electric schedule, service entrance locations, and anchor clip detail.

1.4 	Quality assurance

- Structures shall be the product of a manufacturer with a minimum of 20 years-documented experience in the design and fabrication of portable steel buildings.

- Prefabricated buildings by manufacturers other than the one approved shall submit sufficient data to enable approval to be given. As a minimum: design drawings and/or calculations, applicable certifications, catalog information, and color samples showing equal range of variety.

- Design loads: Live Loads:  Unit to be manufactured to be in full compliance to all codes

for the City & State of installation.  All of these States below have specific Modular

Building requirements that require a 3rd party agency to approve a detailed plan set that

the manufacturer prepares after submittal approval.  The plan set for 3rd party plan review

includes fabrication and weld details, structural and energy calculation all stamped by a

registered PE.  The booth must have the State approval and Insignia prior to shipping.

- States requiring approval.  AL, AZ, CA, CO, FL, GA, ID, IN, MD, MA, MI, NC, NJ, NV,

OH, OR, RI, SC, TN, TX, VA, WA.

# PART 2 - PRODUCTS

2.1	MANUFACTURERS

- Products of the following manufacturer from the basis for design and quality intended.

1.	B.I.G. Enterprises, Inc. South El Monte CA. 800-669-1449

B.	Or equal as approved in accordance with Section 01600 for Substitutions.

  - Structure

- Prefabricated steel building shall be single unit welded construction. Building to be shipped completely assembled. All welded joints ground smooth. Base dimensions to be (Specify Dimensions Here)

- Booth to be designed to meet U.L. 752 standards for Level 10 protection. Booth shall

have this protection in ALL areas from the finished floor height up to the finished ceiling

height. The roof, fascia, overhang, soffit and floor are not protected.  Level 10 is designed

to resist attack from 1 shot from a .50 Caliber Browning using M2-AP 709.5 FMJ

cartridge with a velocity range of 2810-3091 ft\sec.  (Note: AP = Armor Piercing)

B.	4” x 4” x .083” cold drawn electro-welded structural mechanical steel frames.

  - WALLS

A.	16ga. Galvanized steel interior walls and U.L. Level 10 armor plate steel exterior.  Walls to be insulated to R-10 and shall have an additional layer of R-9.6 continuous insulation over the exterior armor plate from floor height to soffit height.  The continuous insulation to be covered by an additional layer of exterior 16ga. galvanized steel panels.  Total wall insulation is R-19.6.  (Note:  Some States require higher R-Value for the walls)

  - Base and floor

A.	Unit to have a 12ga. galvanized steel plate floor welded to a 2” x 2” or 2” x 3” perimeter galvanized steel tube frame with structural galvanized steel joists welded to the frame.  Floor deck to be covered with 20” square black polyvinyl chloride interlocking tiles and a 4” black base cove.

  - Door

- Unit to have one (or two) commercial steel framed insulated sliding doors top hung by eight 3” diameter rigid steel ball bearing rollers from a upper steel track welded in plate, with a lower stainless steel guide, stainless steel pull handles welded to the frame, mortise lock, window and complete weather stripping.  Total door roller system to be rated for 1,000 pounds minimum.

Option: Unit to have a commercial steel framed swing out ballistic door.  Door to have full                                         height stainless steel continuous hinge, stainless steel mortise lever lock and hydraulic closer.

  - Windows

- 16ga. galvanized steel window frame system with flush mounted corners and welded fastening. Unit to have fixed windows on all sides, all windows glazed with U.L. Level 10 tined laminated glass clad polycarbonate.

  - Roof

- Roof to be constructed of internal steel framing and joists with a 16-gauge galvanized roof deck welded to the framing. Roof shall then be coated with a three part Energy Star elastomeric membrane for weather protection with a SRI index of 95 or better.  Roof structure to be insulated to R-19 minimum, and shall have a 10” tall fascia with 6” overhang on all sides.  Roof to slope to drain to rear downspouts and have removable lifting eyes for optional crane offloading and setting. (Note: Some States require higher R-Value for the roof)

  - counter

A.	Booth to have a 2” deep full width galvanized steel at the front wall.  Shelf mounted at 34” A.F.F and painted to match the booth color.

  - Electrical

- Load Center shall be 125 Amp rated 120/240 volt, single phase, 3 wire 12 pole with 40 amp main breaker. Two 120V duplex outlets mounted under the shelf, LED lights recessed in a 16ga. galvanized steel ceiling with single pole wall switch, through the wall mounted air conditioner with 12,000 BTU cooling and 10,600 BTU electric heating at 230 volts.  HVAC to be mounted in a painted steel shroud with louver grill.

WEATHER PROOFING

A.	Weather-tight for exterior use. All seams and joints pressure bonderized. All openings fully weather stripped. Roof shall have heat protective membrane coating.

# PART 3 - EXECUTION

  - General

A.	Install prefabricated buildings on flat and level concrete pad in accordance with the manufacturer's recommendations and placement drawings. Position units over utility stub-ups, verify building is level and anchor.

  - INSTALLATION

A.	Units shall be shipped fully assembled, fully wired, fully glazed and thoroughly painted.

- Position units over electrical stub-up on level pad. Drill and set expansion type anchor bolts.

- Connect power and seal around edges where the floor base meets the concrete pad.

END OF SECTION.